March 15, 2013

KST UHF operation memorandum for the March 15th, 2013 experiment

eiscat  (eiscat@129.242.31.83)

/kst/exp/scans/kst/ni/cp3_ti_pattern.elan

ssh t49851

Experiment name: sp_ni_ti: Resources NI(12)  beata (CP3)

eroshost 129.242.31.100  (t49851)

elan files:eroshost :/kst/exp/ni/beata/beata

Pulse scheme: beata

Start time: 07:00 UT on March 15, 2013  (Friday)

End time: 13:30 UT on March 15, 2013 (extended by 30 min due to failure of beginning at ESR)

Participants: Satonori Nozawa and H. Fujiwara

(Y. Ogawa @ESR)

Before our experiment:

After our experiment: Nothing

Other instruments.

#pointdir 170 3    (<- to remove snow)

#pointdir now 50

EROS:　ssh –f tserver eros u    @129.242.31.83

---------------------------------------------------------------------------

Note: (time in UT)

March 15, 2013

*************************************************************

Clear sky -22 deg

06:35	run /kst/exp/beata/beata fm cp3_ti NI 240  (@eros u)

rtg started

07:00	Tx on

07:00  enablerec

07:02	guisdap –a (at  culebra: 129.242.31.83 (UHF))

13:29	stopexp

Summary

The activity of the ionosphere was low.

Tx was very stable (about 1.6 MW)

DATA were stored at t49851:/data/beata_cp3_ti_2.0u_NI@uhf

Analyzed data were stored at /analysis/results/2013-03-15_beata_ant@uhfa

Descriptions of SP

sp_ni_ti

We aim at investigating variations of ion temperature and electric field in

the F-region (Thermosphere) in order to understand more deeply the basic

state of the Thermosphere as well as the coupling between

Magnetosphere-Ionosphere-Thermosphere in the polar region. We run the Tromso UHF radar and ESR.

PI is Prof Fujiwara.

移動時間30秒弱。

pointrheight 0.0 30.0 $height

setpolariser

DISP "position 1 - EL30 [TimeStamp now] Scan CP3 Ti"

SYNC 120

pointrheight 0.00 60.00 $height

setpolariser

DISP "position 2 - EL60 [TimeStamp now] Scan CP3 Ti"

SYNC 120

pointgeographic 0.0 90.00 $height

setpolariser

DISP "position 3 - EL90 [TimeStamp now] Scan CP3 Ti"

SYNC 120

pointgeographic 0.0 60.00 $height

setpolariser

DISP "position 4 - EL60 [TimeStamp now] Scan CP3 Ti"

SYNC 120