December 11, 2014

KST UHF operation memorandum for the December 11th, 2014 experiment

eiscat

Experiment name: manda

Description: Multi-purpose observations of the D/E/F region ionosphere

Pulse scheme: manda (UHF and VHF)

Start time: 17:00 UT on December 11, 2014  (Thursday)

End time: 23:00 UT on December 11, 2014

Participants: Satonori Nozawa

Before our experiment:

After our experiment: RONE

Other instruments.: LIDAR etc.

---------------------------------------------------------------------------

Note: (time in UT)

Dec 11, 2014

*************************************************************

Clear sky -12 deg

16:30 restart EROSs

eros u kk

eros u

eros v kk

eros v

16:37	run /kst/exp/manda/manda fm zenth NI (@eros v)

16:37	run /kst/exp/ni/manda/manda 1643 cp2_lidar SP (@eros u)

17:00 power on

enablerec

17:17 stopexp (@eros u)

(because the elevations of the two positions are too low (30 deg))

-> we needed to set the reference height (like 240) at the end.

17:18 run /kst/exp/ni/manda/manda 1715 ip2south SP (@eros u)

enablerec

17:20 guisdap –a (@both machines)

-> the both analysis was too slow, could catch up the observations.

Sporadic E-layer around 94 km until around 18 UT.

Aurora in the north

18:00 1244 kw@UHF   1337 kW@VHF

Aurora arc in the north

18:57 1385 kw@UHF, 1434kw@VHF

18:59 -13.5 deg/clear sky

19:49  UHF/VHF down (cronbar etc.)

19:52 1299 kW@UHF

19:57 1433 kW@VHF

20:01 1306 kW@UHF

22:59 stop experiment

Summary

The activity of the ionosphere was moderate or a bit high.

Tx was stable (about 1.3-1.4 MW)

DATA were stored:/data/

manda_ip2south_4.00u_SP@uhf

manda_zenith_4.00v_NI@vhf

Descriptions of SP

PIs: Y. Ogawa

VHF:

We use the Tromso VHF radar with vertical antenna direction and manda pulse code.

UHF:

We use the Tromso UHF radar with scanning mode and manda pulse code.

ip2_south

(180, 77.5) -> (90,90) -> (90,77.5)

360 sec -> 240 sec -> 300 sec

cp2_lidar

(185.8, 77.4) -> (180.0, 90.0) -> Geog. (68.4, 20.0) -> Geog.(68.64, 21.92)

630 sec -> 90 sec -> 90 sec -> 90 sec