December 12, 2014

KST UHF operation memorandum for the December 12th, 2014 experiment

eiscat

Experiment name: manda

Description: Multi-purpose observations of the D/E/F region ionosphere

Pulse scheme: manda (UHF and VHF)

Start time: 17:00 UT on December 12, 2014  (Thursday)

End time: 23:00 UT on December 12, 2014

Participants: Satonori Nozawa

Before our experiment:

After our experiment: RONE

Other instruments.: LIDAR etc.

---------------------------------------------------------------------------

Note: (time in UT)

Dec 12, 2014

*************************************************************

Clear sky -12 deg

16:37	run /kst/exp/ni/manda/manda 1630 cp2_lidar SP 240 (@eros u)

16:47	run /kst/exp/manda/manda fm zenth NI (@eros v)

17:00 power on

17:02 enablerec(@eros v)

guisdap –a @goppi

17:14 stopexp (@eros u)

17:18 run /kst/exp/ni/manda/manda 1630 ip2south SP (@eros u)

17:18 enablerec

guisdap –a @culebra

Aurora in the south-west

19:05 1465 kW@ UHF, 1406 kW@VHF

20:02 1412 kW@UHF, 1442 kW@VHF

20:02 clear sky, -16.8 deg

22:59 stop experiment

Summary

The activity of the ionosphere was moderate or a bit high.

Tx was stable (about 1.3-1.4 MW)

DATA were stored:/data/

manda_ip2south_4.00u_SP@uhf

manda_zenith_4.00v_NI@vhf

Descriptions of SP

PIs: Y. Ogawa

VHF:

We use the Tromso VHF radar with vertical antenna direction and manda pulse code.

UHF:

We use the Tromso UHF radar with scanning mode and manda pulse code.

ip2_south

(180, 77.5) -> (90,90) -> (90,77.5)

360 sec -> 240 sec -> 300 sec

cp2_lidar

(187.03, 77.56) -> (180.0, 90.0) -> Geog. (68.4, 20.0) -> Geog.(68.64, 21.92)

630 sec -> 90 sec -> 90 sec -> 90 sec

how to reset the EROS

(kill)   eros u kk

eros u

(kill)  eros v kk

eros v